IN case of a need to use the Bigboard 2 for a mixed configuration,
(5 1/4 & 8 inch) the following changes must be implemented.

1.	add a 74LS157 on the Bigboard 2 experiment area.
	as follows:

	                    ___ ___
2MC osc   JB35-3    ______2|1a " 1y|4______ 1MC/2MC clock   JB35-2
1Mc osc   JB35-1    ______3|1b     |
Ready/    JB4-3     ______5|2a   2y|7______ Ready/          JB4-2
Gnd	  JB4-1     ______6|2b     |
Wd(U28-11)JB8-3     _____11|3a   3y|9______ WD              JB8-2
Wd(U10-31)JB8-1     _____10|3b	   |
		           |	   |
Select    JB5-1     ______1|sel    |
	                   |       |
                           |74LS157|
	                   |_stb___|
                              |15
          Gnd       __________|              

     pin 16    Vcc
     pin 8     gnd

     pin's  12,13,14  not used (yet)





2.	Make use of a modified Bigboard monitor rom.
	This one is used to initialize a location in the monitor
	ram to start with the floppy drives as indicated by the
	dip switch on the Bigboard 2.
	This location may be altered after boot by the "config"
	program.

          Rom monitor modification:

          Make some room (if needed) by deleting (for example "crcgen").

          In the module "init"  add the following:

          at the point where the disk parameters are set up

          ;
          ;    set disk parameters for 5 or 8 inch drives.
          ;
               in   a,(sense)      ;read dip switch
               bit  5,a            ;test drive type
               jr   z,skip2        ;and jump if 8 inch drives
               ld   a,00000011b
               lä     (dsktyp),á   ;seô disë typå for miné drives

     ;next entry's are addedŠ
               xor  a              ;indicate all drives are 5 1/4 inch
               ld   (typeflag),a   ;this is new
               ld   a,8            ;set mux (74LS157) to 5 1/4 inch
               out  (od9h),a
     skip2:
               call flipdens       ;this is existing code


     ;
     ;    initialize the z-80 for interrupt mode #2


     This is all to be changed in the coding.

     Next changes must me made in the following files:

     memory.mac
     memdef.mac

     at the end of the ram definitions add the following:

     typeflag: defb 00001111b      ;default set to 8 inch
     speed8:   defb 5              ;8 inch seek rate in miliseconds 
     speed5:   defb 3              ;5 1/4 inch seek rate in miliseconds

     Both speed bytes may be modified by the "config" program
     and are used by "autobios" when selecting a drive.

     Assemble the new monitor source, and make a new rom (2732)
     by using the provided "program.com" transient program.

     In order to burn a 2732 eprom,
     Enter: "program rom(cr)."
     Where "rom" is the name of the "com" file to burn in (max 4k)
	     

3.	Assemble the file "autobios" for a mixed configuration
	setup.
	This is done by specifying:

	in "system variables"

	EIGHT	EQU	FALSE 
	FIVE	EQU	FALSE
	MIXED	EQU	TRUE

	The output may then be mixed with a 59K cpm version 2.2
	or smaller if you like.
	The new created bios is to big for a 60K cpm version.


Restrictions.

     All drive selections should be made trough the bios module.Š
     The following programs are known not to do so:

     BB2FORMT.COM
     INIT5.COM

     In absence of the source code these programs are not modified.

     These programs must be executed from the type of drive the program
     is written for.

     I.E.

     Drive "a" = 5 1/4 inch (with your programs bb2formt, init5 etc.)
     Drive "c" = 8 inch

     And you want to initialize an 8 inch floppy in drive "c".

     First insert an initialized 8 inch floppy in drive "c",
     Then log it in.
     Next replace the floppy in "c" by a floppy you want to initialize.
     Then type:

     C>A:BB2FORMT(CR)

     And follow the format menu instructions.

     For 5 inch drives I wrote a format program that will execute
     from either type of drive.
     Thió   wilì  bå  calleä  'format40.com§  oò  'format80.com'¬ 
     depending on a 40 tracks or 80 tracks drive.

	

     You also cannot do an direct sysgen from an 5 1/4 inch drive to
     an 8 inch drive.
     This is due to the fact that the memory layout for the ccp and
     bdos modules are different.

     (see bios.doc)

     You can overcome this problem by reading in either format by the
     corresponding sysgen program, save it as a file, read it back
     using ddt or zid, move the ccp and bdos to the right boundary
     and start the right sysgen to write it back.



            	
	Good luck.

	L.Koopman
	Waarbekenplein 13
	7553 KK Hengelo (o)
	Tel. 074-913022Š	Nederland